Technical Service Bulletin

Reference : Manual revisions - Chrysler vehicle restoration reference manual – Guide to E body fasteners.  Volume: #1 – Version:  # 1

Revision # 4 (Updated 04 July 2005)

Please note the following corrections

| Fastener No. | Ref section | Application | Fastener type | Qty | Thd | A | B | C | D | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 29 B | 4.1 | Torque shaft support bracket | Bolt | 1 | 9/16-12 | .365 | 13/16 Trim | .972 |  |  |
| 114 G | 4.2 | Steering column support plate to fire wall | Bolt | 3 | 5/16-18 | 1.12 | ½ Ind | .75 | .110 | .20 |
| 215 D | 4.3 | Neg. battery cable to engine – small block – 1972 and later | Bolt | 1 | 3/8-16 | .75 | 9/16 Ind | .73 | .10 | .27 |
| 232 | 4.3 | Bottom mounting bolt | Bolt | 2 | 3/8-16 | 1.00 | 9/16 Trim | 2.75 |  |  |
| 229 | 4.3 | Heater hose support bracket | Bolt | 1 | 3/8-16 | .75 | 9/16 Ind | .73 | .10 | .27 |
| 258 D | 4.3 | RH and LH Hemi rubber insulator to bracket nuts. | Marsden Nut | 2 | ½-13 | .45 | 3/4 |  |  |  |
| 401 | 4.4 | 1971 Challenger grille mounting | Bolt | 8 | # 10-24 | .62 | 3/8 Ind | .75 | .08 | .18 |
| 401 | 4.4 | 1971 Challenger grille mounting | U nut | 8 | # 10-24 | .62 |  |  |  |  |
| 407.3 | 4.4 | Head light adapt to fender | Bolt | 8 | ¼-20 | .50 & .75 | 7/16 Ind | .75 | .09 | .18 |
| 460.2 | 4.4 | 1970- and 71 Barracuda / Cuda – Side marker to body nuts | Nut – type 1 | 8 | 3/16” cut | .625 | 7/16 | .80 |  |  |
| 436 | 4.4 | Front fender inner splash shield | Bolt | 2 | 5/16 | 1.00 | .1/2 ind | .82 | .10 | .23 |
| 487.1A | 4.4 | Valance to quarter panel end stud | Stud | 4 | ¼-20 | 1.00 | .30 | .75 |  |  |
| 487.3A | 4.4 | Valance to quarter panel end stud | Stud | 4 | ¼-20 | 1.00 | .30 | .75 |  |  |
| 503 | 4.4 | Axle rebound | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |
| 503 | 4.4 | Muffler heat shield | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |
| 503 | 4.4 | Auto trans splash guard | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |
| 503 | 4.4 | Breather vent line | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |
| 503 | 4.4 | RH ft brake line | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |
| 503 | 4.4 | Plastic shield (K member) | Bolt | 1 | 5/16-18 | .62 | ½ ind | .65 | .08 | .22 |

| Fastener No. | Ref section | Application | Revision / Addition |
| --- | --- | --- | --- |
| N/A | 1.3 | Fastener Engineering specifications – Bolt and screw description | Delete the last paragraph on page # 3. The following table (Section #2) will provide a quick overview of selected components to illustrate how consistent the head markings were ………….. |
| N/A | 3 | Fastener manufacturer ID marking | Blank bolt marking # 267 on pg # 21 should be eliminated. |
| 16 | 41 | Shifter mounting screws | The finish should be Clear zinc & the screws have been found w/& w/o a nylon pallet |
| 17 | 4.1 | Shift level mounting nuts | The finish should be Clear zinc |
| 58.1 B | 4.1 | Axle break line junction block | The finish should be Clear Zinc or Zinc (yellow) dichromate |
| 58.2 B | 4.1 | Axle break line junction block | The finish should be Clear Zinc or Zinc (yellow) dichromate |
| 60 | 4.1 | Dana 60 series axle-oil fill plug | Delete the statement (prior to paint). This plug is not painted. |
| 102 | 4.2 | Idler arm to K frame 1973 -74 | Other head marking found # 104 |
| 108 D | 4.2 | Front shock absorber mounting | The finish should be galvanized. |
| 203.2A | 4.3 | Wing nut - solid | The finish should be chrome plated |
| 206 | 4.3 | Carburetor choke assembly mounting bolts | There is only (1) fastener required for small block applications between 1972 – 74 in lieu of (2). |
| 220 | 4.3 | Ex. Man to cylinder head - Hemi | Quantity should be (11) |
| 221 | 4.3 | Exhaust manifold to cylinder head fasteners big block | Fastener D. Sleeve nuts – 1970 should read (1) 3/8-24 x 1.95” lg. sleeve nut. In lieu of (2). |
| Fastener No. | Ref section | Application | Revision / Addition |
| 266B | 4.3 | Starter to bell housing stud | The finish should be zinc |
| 402 | 4.4 | Chal & Barracuda ralley hood scoop insert to hood screws | The finish should be Zinc (yellow) dichromate |
| 409.1 | 4.4 | Barracuda grille to header | The finish could be also be Zinc (yellow) dichromate |
| 409.2 | 4.4 | Barracuda grille to header * | Lower bolts thread into pinch weld insert on support bracket |
| 439 | 4.4 | Electrical component mounting | The finish should be Silver Zinc |
| 440 B & C | 4.4 | Starter relay wire mounting | The finish could also be Zinc (yellow) dichromate |
| 447 | 4.4 | Main wiring bulkhead mounting | The finish should be galvanized. |
| 449 | 4.4 | Head light wire harness holder | The finish should be galvanized. |
| 460.1,2 & 3 | 4.4 | Side marker fasteners | The finish should be galvanized. |
| 460.2 | 4.4 | 1970- and 71 Barracuda / Cuda – Side marker to body nuts | Page # 297. The text should read (8) 3/16” cut thread type 1 Achorn hex nuts. |
| 461 | 4.4 | Cowl screen mounting screws | Page # 298. A and B screws. The 295 in the description was placed there in error. Please disregard the 295. |
| 463 B | 4.4 | Wiper arm bracket to wiper motor | The description in the lower right of the page should rear as follows: Wiper arm bracket to wiper motor. |
| 464 E | 4.4 | Emergency (park) brake mounting | The finish should be Red chromate |
| 465.1 | 4.4 | Upper dash frame to cowl | The finish could be Phosphate or Clear zinc |
| 465.2 | 4.4 | Dash frame to A pillar | The finish could be Phosphate or Clear zinc |
| 482.1 B & C | 4.4 | Challenger tail lights | The finish should be galvanized. |
| 482.3 | 4.4 | Challenger tail lights housing | The finish should be galvanized. |
| 486.5C | 4.4 | Rear bumper guard mounting fasteners - retainer | The finish should be Copper plating |
| 488 B | 4.4 | Rear bumper support bracket | The finish should be Copper plating |
| 488 C | 4.4 |  | The finish could also be Clear zinc. |
| 513 A | 4.4 | Gas tank strap - Nut | The finish could also be Clear zinc |
| 513 B | 4.4 | Gas tank strap - Bolt | The finish could also be Zinc (yellow) dichromate |

# Text boxes

Moparr Motors – Detroit

P.O. Box 210074

Auburn Hills, MI 48321

248-393-3970

Notes: