Technical Service Bulletin

Reference : Manual revisions - Chrysler vehicle restoration reference manual – Guide to B body Dodge fasteners.  Volume: #2 – Version:  # 2

Revision # 1 (Updated 02 December 2006)

Please note the following corrections :

| Fastener No. | Ref section | Application | Fastener type | Qty | Thd | A | B | C | D | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 258D | 4.3 | RH and LH rubber insulator to bracket nuts | Marsden Nut | 2 | ½-13 | .32 | 3/4 |  |  |  |
| 259 C | 4.3 | RH insulator to K member nuts | Nut | 2 | ½-13 | 1.25 | 3/4 | .42 | .14 |  |

| Fastener No. | Ref section | Application | Revision / Addition |
| --- | --- | --- | --- |
| 258D | 4.3 | RH and LH rubber insulator to bracket nuts | The description of the nut should read (2) ½-13 Hex Marsden nuts. Phosphate finished (Prior to paint) |
| 259 C | 4.3 | RH insulator to K member nuts | The description of the nut should read (2) ½-13 Hex Coni Keps nuts. Phosphate finished |

# Text boxes

Moparr Motors – Detroit

P.O. Box 210074

Auburn Hills, MI 48321

248-393-3970

Notes: